eV=qVo

7.1
LED energy band diagrams
.
draw=todo

7.2
short circuit GaAs solar cell
photon flux=No=1.8E17/cm2-s
Isc=qNo=2.88E2 Acm-2
Voc=(kt/q)ln(Isc/Io)=1.04V
Io=dark current=1E-19Acm-2
Pmax=Isc*Voc*FF=2.4E-2Wcm-2
FF=fill factor=.8

7.3
0.32 is max efficiency because if the band gap is too high it doesn’t get enough absorbtion. Too low gaps have thermal loss

6.1
metal/n-GaAs system
metal work function=4.9 eV
Electron affinity GaAs=4 eV
Doping GaAs=1E16cm-3
Nc=5E17cm-3
Eg GaAs=1.42eV
.
draw=TODO
Vo=TODO
W=sqrt(2ϵ Vo/q Nd)
ϵ=ϵ0*ϵR
C/A=ϵ/W

6.2
repeat, p-type GaAs
metwal work function=4.3eV
p-doping=1E17cm-3
Nv=1.5E19cm-3
.
draw
Vo

6.3
n/n heterojunctions
S1: Bandgap=2ev , ΔECF = 0.1eV , Electron Affinity= 3.9eV
S2: Bandgap=1.4ev , ΔECF = 0.2eV , Electron Affinity= 4.2eV
.
Draw=TODO
calculate built in voltage

6.4
p/n heterojunctions
same as before but S1 is p doped

5.1
GaAs p-n junctions. Use fermi method
NA=1E17cm-3
ND=1E16cm-3
Nc=4.2E17cm-3
Nv=9.5E18cm-3
.
ΔECF=0.97eV on n side
ΔEFV=0.118eV on p side
Vo=1.42-ΔECF-ΔEFV=1.21eV
Vo=1.21V

5.2
TODO-5.1 vars change at 500K

5.3
Si p+n junction (which means that p is much more heavily doped than n side)
n doping=1E16cm-3
calc W (depletion region)
.
W=sqrt(2ϵ Vo/q Nd)
Vo=0.814V
Wv=0 = 3.25E-5cm
Wv=0.5 = 2.02E-5cm
Wv=-5 = 8.69E-5cm

5.4

5.5

p-n junctions

Equilibrium: Vo=(kt/q)ln(pp/pn)=(kt/q)ln(Na*Nd/ni*ni)
pp/pn=nn/np=exp(qVo/kT)
W=sqrt((2ϵ(Vo-V)/q)*(Na+Nd / Na*Nd))
Vo=q*Nd*W2 / 2ϵ
Ideal diode = I=Io*exp(qV/kt)-Io
C/A=ϵ/W

1.

pn junction band diagrams
pn junction carrier concentration
pn forward and reverse bias
diode current equation
tunnel diode I-V curve
Schottky barrier height
heterojunction band diagrams
heterojunction built in voltages
current in a solar cell
efficient LED